## Slide 1
facebook.com/fibre.project
@FIBRE_project
This work makes use of results produced by the FIBRE project, co-funded by the Brazilian Council for Scientific and Technological Development (CNPq) and by the European Commission within its Seventh Framework Programme.
www.fibre-ict.eu
EXPERIMENTAL ISLANDS
FIBRE - Intercontinental Testbed for Future Internet Experimentation
Sebastia Sallent1, Antonio Abelém2, Iara Machado3, Leonardo Bergesio1, Serge Fdida4, José Rezende5, Dimitra Simeonidou6, Marcos Salvador7, Leandro Ciuffo3, Leandros Tassiulas8 and Carlos Bermudo1
1 {sebastia.sallent, leonardo.bergesio, carlos.bermudo}@i2cat.net | 2 abelem@ufpa.br | 3 {iara, leandro.ciuffo}@rnp.br | 4 serge.fdida@lip6.fr | 5 rezende@land.ufrj.br | 6 dsimeo@essex.ac.uk | 7 marcosrs@cpqd.com.br | 8 leandros@uth.br
Situation as of May 2013
UFF
UFRJ
UFSCar
CPqD
UNIFACS
UFPE
UFG
UFPA
RNP
USP
U.Bristol
I2CAT
UTH
BRAZIL
EUROPE
NETWORK LIGHTPATHS
A TYPICAL BRAZILIAN ISLAND
EUROPEAN ISLANDS
Bristol
i2CAT
i2CAT (Spain)
With the globalization of experimental FI research, there has been considerable interest in the federation of distinct testbed facilities, in order to permit carrying out experiments that span multiple testbeds. Federation is a key issue in the design of the FIBRE testbed, which is being deployed as a federation of 13 local experimental facilities (a.k.a. “islands”).
CONTROL FRAMEWORKS
OFELIA Control Framework (OCF) was originally created in the context of the OFELIA testbed project [www.fp7-ofelia.eu] but today it is supported by a larger community where FIBRE and GEANT are present. OCF is synchronized with other initiatives in USA (GENI) and follows an SFA-oriented architecture (Slice-based Facility Architecture).
OMF is a framework with the focus on controlling and managing network devices. It was developed based on XMPP in the Ruby language. The OMF suite also provides OML (OMF Monitoring Library), which allows instrumentation of applications for collecting measurements.
ProtoGENI is a control and monitoring based on an enhanced version of the Emulab management software. The Emulab testbed is used to perform experimental research on distributed systems. ProtoGENI was created to provide the integration between Emulab and other testbeds in order to build the Cluster C facility of GENI.
Red IRIS
AMPATH
The physical interconnection of Brazilian and European islands is deployed through two point-to-point circuits (a.k.a. lightpaths) linking FIBRE´s Brazilian gateway at the University of Sao Paulo (USP, Brazil) to i2CAT (Spain) and University of Bristol (UK), spanning multiple network domains.
1GbE
DWDM ring
Barcelona
SuperMicro 6016T-T Servers
Pronto TN3290
Switches
Linksys WRT54GL
Wi-Fi routers
To RedIris and RNP (Brazil)
1GbE
ROADM
ROADM
ROADM
To UnivBRIS and NITOS
To OFELIA island (i2CAT)
100MbE
UTH (Greece)
U. Bristol (UK)
NetFPGA #1
NetFPGA #3
NetFPGA #2
Pica8 Pronto Switch
IBM server
(VMs, LDAP)
Datacom OpenFlow switch
(FIBREnet border router)
. . .
Icarus node #1
Icarus node #8
Wireless Network (OMF domain)
Top of Rack
conventional
switch
Data plane link
Control plane link
Data + Control plane
Wireless experimental facility
OFELIA Control Framework
OMF
ProtoGENI
WDM GMPLS
UFRJ
UFF
RNP
PoP-RJ
PoP-DF
PoP-GO
PoP-BA
PoP-PA
PoP-PE
UFPE
OMF
OCF
UFPA
UNIFACS
OMF
OCF
UFG
OCF
OMF
OCF
OMF
OCF
UFSCar
OMF
OCF
USP
Proto
GENI
OMF
OCF
PoP-SP
i2CAT
OCF
U. Bristol
OCF
UTH
OMF
WDM
PoP-i2CAT
PoP-UTH
PoP-UB
CPqD
OMF
OCF
WDM
OMF
OCF
OMF
OCF